## Slide 1
BASIC COMPUTER ORGANIZATION AND DESIGN

## Slide 2
BASIC COMPUTER ORGANIZATION AND DESIGN
• Timing and Control
• Instruction Cycle

## Slide 3
TIMING AND CONTROL
Control unit of Basic Computer
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8
decoder
7 6 5 4 3 2 1 0
I
D
0
15 14 . . . . 2 1 0
4 x 16
decoder
4-bit
sequence
counter
(SC)
Increment (INR)
Clear (CLR)
Clock
Other inputs
Control
signals
D
T
T
7
15
0
Combinational
Control
logic

## Slide 4
TIMING SIGNALS
- Generated by 4-bit sequence counter and 4×16 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.
D3T4: SC ← 0

## Slide 5
INSTRUCTION CYCLE
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory
  Decode the instruction and calculate effective address (EA)
  Read the EA from memory if the instruction has an indirect address
  (Fetch operand)
  Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction
Note: Every different processor has its own (different) instruction cycle

## Slide 6
DETERMINE THE TYPE OF INSTRUCTION
= 0 (direct)
D'7IT3: AR ← M[AR]
D'7I'T3: Nothing
D7I'T3: Execute a register-reference instr.
D7IT3: Execute an input-output instr.
Start
SC ← 0
AR
←
PC
T0
IR
←
M[AR],
PC
←
PC + 1
T1
AR
←
IR(0-11),
I
←
IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference) =>opcode ≠ 111
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC
←
0
Execute
input-output
instruction
SC
←
0
M[AR]
←
AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC
←
0
T4

## Slide 7
REGISTER REFERENCE INSTRUCTIONS
r = D7 I′T3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Register Reference Instructions are identified when
r: SC ← 0
CLA rB11: AC ← 0
CLE rB10: E ← 0
CMA rB9: AC ← AC’
CME rB8: E ← E’
CIR rB7: AC ← shr AC, AC(15) ← E, E ← AC(0)
CIL rB6: AC ← shl AC, AC(0) ← E, E ← AC(15)
INC rB5: AC ← AC + 1
SPA rB4: if (AC(15) = 0) then (PC ← PC+1)
SNA rB3: if (AC(15) = 1) then (PC ← PC+1)
SZA rB2: if (AC = 0) then (PC ← PC+1)
SZE rB1: if (E = 0) then (PC ← PC+1)
HLT rB0: S ← 0 (S is a start-stop flip-flop)