## Slide 1
TOPIC:
RISC and CISC Characteristics
(Lecture 33-34)

## Slide 2
RISC and CISC

## Slide 3: RISC and CISC
Reduced Instruction Set Architecture (RISC) – The main idea behind this is to make hardware simpler by using an instruction set composed of a few basic steps for loading, evaluating, and storing operations just like a load command will load data, a store command will store the data.
In the early 1980s, a number of computer designers recommended that computers use fewer instructions with simple constructs so they can be executed much faster within the CPU without having to use memory as often. This type of computer is classified as a reduced instruction set computer or RISC.

## Slide 4: RISC and CISC (Cont.)
Complex Instruction Set Architecture (CISC) – The main idea is that a single instruction will do all loading, evaluating, and storing operations just like a multiplication command will do stuff like loading data, evaluating, and storing it, hence it’s complex.
The trend into computer hardware complexity was influenced by various factors, such as upgrading existing models to provide more customer applications, adding instructions that facilitate the translation from high-level language into machine language programs, and striving to develop machines that move functions from software implementation into hardware implementation. A computer with a large number of instructions is classified as a complex instruction set computer, abbreviated CISC.

## Slide 5: RISC and CISC (Cont.)
Both approaches try to increase the CPU performance .
RISC: Reduce the cycles per instruction at the cost of the number
of instructions per program.
CISC: The CISC approach attempts to minimize the number of
instructions per program but at the cost of an increase in
the number of cycles per instruction.

## Slide 6
Characteristic of RISC

## Slide 7: Characteristic of RISC
Earlier when programming was done using assembly language, a need was felt to make instruction do more tasks because programming in assembly was tedious and error-prone due to which CISC architecture evolved but with the uprise of high-level language dependency on assembly reduced RISC architecture prevailed.
Characteristic of RISC –
Relatively few instructions.
Relatively few addressing modes.
Memory access limited to load and store instructions.
All operations done within the registers of the CPU.
Fixed-length, easily decoded instruction format.
Single-cycle instruction execution.
Hardwired rather than micro-programmed control.

## Slide 8
Characteristic of CISC

## Slide 9: Characteristic of CISC
Characteristic of CISC –
The major characteristics of CISC architecture are:
A large number of instructions-typically from 100 to 250 instructions.
Some instructions that perform specialized tasks and are used infrequently.
A large variety of addressing modes-typically from 5 to 20 different modes.
Variable-length instruction formats.
Instructions that manipulate operands in memory.
Examples of CISC architectures are the Digital Equipment Corporation VAX computer and the IBM 370 computer.

## Slide 10: Continue..
Example – Suppose we have to add two 8-bit numbers:
CISC approach: There will be a single command or instruction for this like ADD which will perform the task.
RISC approach: Here programmer will write the first load command to load data in registers then it will use a suitable operator and then it will store the result in the desired location.
So, add operation is divided into parts i.e. load, operate, store due to which RISC programs are longer and require more memory to get stored but require fewer transistors due to less complex command.

## Slide 11
Differences RISC and CISC

## Slide 12: Differences RISC and CISC
RISC | CISC
Focus on software | Focus on hardware
Uses only Hardwired control unit | Uses both hardwired and microprogrammed control unit
Transistors are used for more registers | Transistors are used for storing complex Instructions
Fixed sized instructions | Variable sized instructions
Can perform only Register to Register Arithmetic operations | Can perform REG to REG or REG to MEM or MEM to MEM
Requires more number of registers | Requires less number of registers
Code size is large | Code size is small
An instruction executed in a single clock cycle | Instruction takes more than one clock cycle
An instruction fit in one word | Instructions are larger than the size of one word

## Slide 13
THANK YOU